## Slide 1: Implementation of a Convolutional Neural Network on an FPGA
Dresden, 19.10.2018
Binyi Wu
Faculty of Electrical and Computer Engineering Chair of Highly-Parallel VLSI Systems and Neuro-Microelectronics

## Slide 2: Content
Motivation
Convolutional Neural Networks (CNNs)
Architecture of Convolutional Neural Network Accelerator (CNNA)
Validation and Experiment
Conclusion

## Slide 3: Content
Motivation
Convolutional Neural Networks (CNNs)
Architecture of Convolutional Neural Network Accelerator (CNNA)
Validation and Experiment
Conclusion

## Slide 4: Motivation
Convolutional neural networks (CNNs)
  (+): achieve near or even beyond human performance
  (-): at the cost of high computational complexity.
  Making running CNNs in mobile device impossible
  -> Design a CNN Accelerator (CNNA)

## Slide 5: Content
Motivation
Convolutional Neural Networks (CNNs)
Architecture of Convolutional Neural Network Accelerator (CNNA)
Validation and Experiment
Conclusion

## Slide 6: Convolutional Neural Networks (CNNs)
  Structure of CNNs
CONV
FC
POOL
NONL
CONV
NONL
CONV
NONL
POOL
LOSS
Input Layer
Hidden Layer
Hidden Layer
Output Layer
CONV: convolutional layer
NONL: non-linearity layer
POOL: pooling layer
FC: fully connected layer
LOSS: loss layer
Computation Amount: CONV >> Other Layers

## Slide 7: Convolutional Neural Networks (CNNs)
  CONV: convolutional layer
Filters_1
Neuron Activation
(NA)
Filters_2
Filters_3

## Slide 8: Convolutional Neural Networks (CNNs)
100 | 101 | 102 | 103 | 104
110 | 111 | 112 | 113 | 114
120 | 121 | 122 | 123 | 124
130 | 131 | 132 | 133 | 134
140 | 141 | 142 | 143 | 144
  CONV: Convolutional Operation (stride = 1)
000 | 001 | 002 | 003 | 004
010 | 011 | 012 | 013 | 014
020 | 021 | 022 | 023 | 024
030 | 031 | 032 | 033 | 034
040 | 041 | 042 | 043 | 044
100 | 101 | 102
110 | 111 | 112
120 | 121 | 122
000 | 001 | 002
010 | 011 | 012
020 | 021 | 022
113190 | 114288 | 115386
124170 | 125268 | 126366
135150 | 136248 | 137346
Neuron activation:
Filter:
Sum over element-wise multiplication

## Slide 9: Convolutional Neural Networks (CNNs)
100 | 101 | 102 | 103 | 104
110 | 111 | 112 | 113 | 114
120 | 121 | 122 | 123 | 124
130 | 131 | 132 | 133 | 134
140 | 141 | 142 | 143 | 144
  CONV: Convolutional Operation (stride = 1)
000 | 001 | 002 | 003 | 004
010 | 011 | 012 | 013 | 014
020 | 021 | 022 | 023 | 024
030 | 031 | 032 | 033 | 034
040 | 041 | 042 | 043 | 044
100 | 101 | 102
110 | 111 | 112
120 | 121 | 122
000 | 001 | 002
010 | 011 | 012
020 | 021 | 022
113190 | 114288 | 115386
124170 | 125268 | 126366
135150 | 136248 | 137346
Neuron activation:
Filter:
Sum over element-wise multiplication
stride=1

## Slide 10: Convolutional Neural Networks (CNNs)
100 | 101 | 102 | 103 | 104
110 | 111 | 112 | 113 | 114
120 | 121 | 122 | 123 | 124
130 | 131 | 132 | 133 | 134
140 | 141 | 142 | 143 | 144
  CONV: Convolutional Operation (stride = 1)
000 | 001 | 002 | 003 | 004
010 | 011 | 012 | 013 | 014
020 | 021 | 022 | 023 | 024
030 | 031 | 032 | 033 | 034
040 | 041 | 042 | 043 | 044
100 | 101 | 102
110 | 111 | 112
120 | 121 | 122
000 | 001 | 002
010 | 011 | 012
020 | 021 | 022
113190 | 114288 | 115386
124170 | 125268 | 126366
135150 | 136248 | 137346
Neuron activation:
Filter:
Sum over element-wise multiplication
stride=1
stride=1

## Slide 11: Convolutional Neural Networks (CNNs)
100 | 101 | 102 | 103 | 104
110 | 111 | 112 | 113 | 114
120 | 121 | 122 | 123 | 124
130 | 131 | 132 | 133 | 134
140 | 141 | 142 | 143 | 144
  CONV: Convolutional Operation (stride = 1)
000 | 001 | 002 | 003 | 004
010 | 011 | 012 | 013 | 014
020 | 021 | 022 | 023 | 024
030 | 031 | 032 | 033 | 034
040 | 041 | 042 | 043 | 044
100 | 101 | 102
110 | 111 | 112
120 | 121 | 122
000 | 001 | 002
010 | 011 | 012
020 | 021 | 022
113190 | 114288 | 115386
124170 | 125268 | 126366
135150 | 136248 | 137346
Neuron activation:
Filter:
Sum over element-wise multiplication
stride=1
stride=1

## Slide 12: Convolutional Neural Networks (CNNs)
100 | 101 | 102 | 103 | 104
110 | 111 | 112 | 113 | 114
120 | 121 | 122 | 123 | 124
130 | 131 | 132 | 133 | 134
140 | 141 | 142 | 143 | 144
  CONV: Convolutional Operation (stride = 1)
000 | 001 | 002 | 003 | 004
010 | 011 | 012 | 013 | 014
020 | 021 | 022 | 023 | 024
030 | 031 | 032 | 033 | 034
040 | 041 | 042 | 043 | 044
100 | 101 | 102
110 | 111 | 112
120 | 121 | 122
000 | 001 | 002
010 | 011 | 012
020 | 021 | 022
113190 | 114288 | 115386
124170 | 125268 | 126366
135150 | 136248 | 137346
Neuron activation:
Filter:
Sum over element-wise multiplication
stride=1
stride=1

## Slide 13: Convolutional Neural Networks (CNNs)
  CONV: Data Reuse - Filter

## Slide 14: Convolutional Neural Networks (CNNs)
  CONV: Data Reuse - Filter
filter is reused 9 times

## Slide 15: Convolutional Neural Networks (CNNs)
  CONV: Data Reuse – Neuron Activation
Most elements are used more than one times.

## Slide 16: Convolutional Neural Networks (CNNs)
  CONV: Data Reuse – Neuron Activation
NA
Filters
NA: reused 4 times

## Slide 17: Convolutional Neural Networks (CNNs)
  FC: Mathematical Operation
  Matrix Multiplication

## Slide 18: Convolutional Neural Networks (CNNs)
  FC: Data Reuse
  Each row of is reused multi-times by columns of .
  2. is reused multi-times by rows of .

## Slide 19: Content
Motivation
Convolutional Neural Networks (CNNs)
Architecture of Convolutional Neural Network Accelerator (CNNA)
Validation and Experiment
Conclusion

## Slide 20: Architecture of CNNA
  Architecture Concept
Data Reuse

## Slide 21: Architecture of CNNA
  CNNA System
CPU
CNN
Accelerator
(CNNA)
Memory
cnna_start
cnna_finish

## Slide 22: Architecture of CNNA
  CNNA Limitation
CNNA can only accelerate
- convolutional layer (CONV)
- and fully-connected layer (FC).

## Slide 23: Architecture of CNNA
  General Architecture
CNNA Control Unit
Distributor
Quad Computation Unit Set
Memory Control/
Data In (128-bit)
CPU CNNA Interface
Memory Data Out
(512-bit)

## Slide 24: Architecture of CNNA
  CNNA Control Unit
CNNA Control Unit
Distributor
Quad Computation Unit Set
Memory Control/
Data In (128-bit)
CPU CNNA Interface
Memory Data Out
(512-bit)

## Slide 25
FSM
Control Logic
Configuration
Register
Set
mem_rd_data(128)
Address Generator
cpu_to_cnna
CNNA Control Unit
mem_addr(8)
NA: Neuron Activation
mem_rd_en
CNNA Control Unit
Start and configuration Phase

## Slide 26
FSM
Control Logic
Configuration
Register
Set
Address Generator
CNNA Control Unit
NA: Neuron Activation
CNNA Control Unit
Layer Reset Phase

## Slide 27
FSM
Control Logic
Configuration
Register
Set
mem_rd_data(128)
NA Load
Control
NA Fetch Control
Address Generator
Computation
Unit
Control
Filter Load
control
CNNA Control Unit
mem_addr(8)
NA: Neuron Activation
mem_rd_en
mem_wr_en
“Distributor”
CNNA Control Unit
“Distributor”
Filter Load Phase
All filters will be completed cached.

## Slide 28
FSM
Control Logic
Configuration
Register
Set
mem_rd_data(128)
NA Load
Control
NA Fetch Control
Address Generator
Computation
Unit
Control
Filter Load
control
CNNA Control Unit
mem_addr(8)
NA: Neuron Activation
mem_rd_en
“Distributor”
CNNA Control Unit
“Distributor”
Neuron Activation (NA) Load Phase
As the NA Cache is not large enough, only part of NA will be cached.

## Slide 29
FSM
Control Logic
Configuration
Register
Set
mem_rd_data(128)
NA Load
Control
NA Fetch Control
Address Generator
Computation
Unit
Control
Filter Load
control
CNNA Control Unit
mem_addr(8)
NA: Neuron Activation
mem_rd_en
mem_wr_en
“Distributor”
“Distributor”
“Distributor”
CNNA Control Unit
“Distributor”
NA Fetch and Compute Phase
NA Fetch
Compute
Write result
Load the remaining NA
Memory read and write operations are staggered from each other.

## Slide 30
FSM
Control Logic
Configuration
Register
Set
NA Load
Control
NA Fetch Control
Address Generator
Computation
Unit
Control
Filter Load
control
CNNA Control Unit
NA: Neuron Activation
CNNA Control Unit
CNNA finish Phase
cnna_to_cpu

## Slide 31
CNNA Control Unit: FSM
From Configuration Register Set

## Slide 32
CNNA Control Unit: FSM

## Slide 33: Architecture of CNNA
  Distributor
CNNA Control Unit
Distributor
Quad Computation Unit Set
Memory Control/
Data In (128-bit)
Memory Data Out
(512-bit)

## Slide 34: Architecture of CNNA
  Distributor
  Distribute signal (e.g. memory data) to 16 Computation Units; Each unit occupies 8-bit memory bus.
  Control signal gating to 16 Computation Units, saving power consumption.

## Slide 35: Architecture of CNNA
  Quad Computation Unit Set
CNNA Control Unit
Distributor
Quad Computation Unit Set
Memory Control/
Data In (128-bit)
Memory Data Out
(512-bit)

## Slide 36
NA Fetch Unit
MAC Array
Unit
NA Cache
Filter Weight Cache
Computation Unit
TF Adder
Array
Unit
“NA Load Control”
“NA Fetch Control”
“Computation Unit Control”
“Filter Load Control”
…
1st result
Operand Fetch
Control
…
TensorFlow
Quantization
Unit
mac_en
2nd result
3rd result
4th result
5th result
16th result
…
…
1st filter, Xthchannel
2nd filter, Xth channel
3rd filter, Xth channel
4th filter, Xth channel
5th filter, Xth channel
…
16th filter, Xth channel
cu_control
“memory bus”(8-bit)
Computation Unit
Determine if NA is 0 to choose the next operation:
Skip and wait for next NA
Computing
16 MACs

## Slide 37
Computation Unit
“Distributor”
control signal
Computation Unit
“Distributor”
control signal
Computation Unit
“Distributor”
control signal
Computation Unit
“Distributor”
control signal
Quad Computation Unit
Accumulator Adder
Quad Computation Unit

## Slide 38
Quad
Computation Unit
“Distributor”
control signal
Quad
Computation Unit
“Distributor”
control signal
Quad
Computation Unit
“Distributor”
control signal
Quad
Computation Unit
“Distributor”
control signal
Quad Computation Unit Set
Accumulator Adder
4 x 4 = 16 Computation Units
Computation Unit
“Distributor”
control signal
Computation Unit
“Distributor”
control signal
Computation Unit
“Distributor”
control signal
Computation Unit
“Distributor”
control signal
Quad Computation Unit
Accumulator Adder
Quad Computation Unit Set

## Slide 39: Content
Motivation
Convolutional Neural Networks (CNNs)
Architecture of Convolutional Neural Network Accelerator (CNNA)
Validation and Experiment
Conclusion

## Slide 40: Validation and Experiment
  Validation System
FPGA
CNNA
SRAM-I
(128-bit)
SRAM-O
(512-bit)
DATA
DATA
UDP Controller
DATA
DATA
Validation Program
(Python, TensorFlow, UDP protocol )
cnna_begin
cnna_end

## Slide 41: Validation and Experiment
  Validation System
FPGA
CNNA
SRAM-I
(128-bit)
SRAM-O
(512-bit)
DATA
DATA
UDP Controller
DATA
DATA
Validation Program
(Python, TensorFlow, UDP protocol )
cnna_begin
cnna_end

## Slide 42: Validation and Experiment
  CONV Mapping: Data Dimension
…
NA

## Slide 43: Validation and Experiment
  CONV Mapping: Limitation
Limited by the number of Computation Units
Limited by NA Cache
Limited by the number of Computation Units
Limited by the number of MACs in a Computation Unit
stride = 1
Limited by Filter Cache
=

## Slide 44
CONV Mapping
filter_0, channel_0
filter_1, channel_0
filter_2, channel_0
…
filter_15, channel_0
NA, channel_0
MAC_0
MAC_1
MAC_2
…
MAC_15
AA_0
AA_1
AA_2
…
AA_15
filter_0, channel_1
filter_1, channel_1
filter_2, channel_1
…
filter_15, channel_1
NA, channel_1
MAC_0
MAC_1
MAC_2
…
MAC_15
filter_0, channel_15
filter_1, channel_15
filter_2, channel_15
…
filter_15, channel_15
NA, channel_15
MAC_0
MAC_1
MAC_2
…
MAC_15
…
CU_15
CU_1
CU_0
QA_0
QA_1
QA_2
…
QA_15
QA_0
QA_1
QA_2
…
QA_15
QA_0
QA_1
QA_2
…
QA_15
…
NA
Part of NA will be cached.
Filters need to be fully cached.

## Slide 45: Validation and Experiment
  Benchmark: CONV
computation clocks >> prefetch clocks
Acceleration: up to around 100
Bottleneck: Computing resource

## Slide 46: Validation and Experiment
  Benchmark: CONV
computation clocks >> prefetch clocks
Acceleration: up to around 100
Bottleneck: Computing resource

## Slide 47: Validation and Experiment
  Benchmark: CONV
computation clocks >> prefetch clocks
Acceleration: up to around 100
Bottleneck: Computing resource

## Slide 48: Validation and Experiment
  Benchmark: CONV
computation clocks >> prefetch clocks
Acceleration: up to around 150
-> More MACs are used
Bottleneck: Computing resource

## Slide 49: Validation and Experiment
  Benchmark: CONV
computation clocks >> prefetch clocks
Acceleration: up to around 300
-> More MACs are used
Bottleneck: Computing resource

## Slide 50: Validation and Experiment
  FC Mapping
…
b [N, M]
 |  |  | … | 
N
N
M
M
a [1, N]
r [1, M]
elements are separated into parts.
Each column has elements and separated into parts.
Each part has elements.
Each part has elements.
!!! don’t muss be equal to

## Slide 51: Validation and Experiment
  FC Mapping: Limitation

## Slide 52
FC Mapping
b[0], part_0
b[1], part_0
b[2], part_0
…
b[15], part_0
a, part_0
MAC_0
MAC_1
MAC_2
…
MAC_15
AA_0
AA_1
AA_2
…
AA_15
b[0], part_1
b[1], part_1
b[2], part_1
…
b[15], part_1
a, part_1
MAC_0
MAC_1
MAC_2
…
MAC_15
b[0], part_15
b[1], part_15
b[2], part_15
…
b[15], part_15
a, part_15
MAC_0
MAC_1
MAC_2
…
MAC_15
…
CU_15
CU_1
CU_0
QA_0
QA_1
QA_2
…
QA_15
QA_0
QA_1
QA_2
…
QA_15
QA_0
QA_1
QA_2
…
QA_15
…
a [1, N]
b [N, M]
 |  |  | … | 
N
N
M
M
a [1, N] muss be fully cached.
b [N, M] muss be fully cached.

## Slide 53: Validation and Experiment
  Benchmark: FC
: The size of each part is variable.
prefetch clocks >> computation clocks
Acceleration: up to around 7
Bottleneck: memory bandwidth

## Slide 54: Validation and Experiment
  Benchmark: FC
Number of columns of is variable.
prefetch clocks >> computation clocks
Acceleration: up to around 7
Bottleneck: memory bandwidth

## Slide 55: Validation and Experiment
  Benchmark: FC
Number of parts is variable.
prefetch clocks >> computation clocks
Acceleration: up to around 13
Bottleneck: memory bandwidth

## Slide 56: Content
Motivation
Convolutional Neural Networks (CNNs)
Architecture of Convolutional Neural Network Accelerator (CNNA)
Validation and Experiment
Conclusion

## Slide 57: Conclusion
  Bottleneck: CONV-computing resources, FC-memory bandwidth
  Utilization of the data reusing through
  - using cache of NA and filter;
  - putting computing resources, which share same data, in a unit.
  reduce power consumption as much as possible through
  - reducing memory operation;
  - skipping multiplication by 0.

## Slide 58: Conclusion
  Improvement
  Start to compute during pre-caching
  Optimize the cache size, enable cache sharing
  Support other stride
  Add padding layer, pooling layer etc.
  …

## Slide 59
Thank you for your attention!

## Slide 60
Configuration

## Slide 61: Architecture of CNNA
  CNNA Control Unit: Configuration Register Set
How to set the value for registers?
Register Description

## Slide 62
Memory

## Slide 63: Architecture of CNNA
  Memory Arrangement
Configuration Data

## Slide 64
NA Cache

## Slide 65
NA Cache
32 x 7 = 224 Bytes

## Slide 66
NA Cache
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
filter
neuron activation

## Slide 67
NA Cache
1 | 2 | 3 | 4 | 5 | 6 | 7
11 | 12 | 13 | 14 | 15 | 16 | 17
21 | 22 | 23 | 24 | 25 | 26 | 27
11 | 12 | 13 | 14 | 15 | 16 | 17
1 | 2 | 3 | 4 | 5 | 6 | 7
Pre-Caching
Channel 0
Channel 6
NA Cache
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
neuron activation

## Slide 68
NA Cache
1 | 2 | 3 | 4 | 5 | 6 | 7
11 | 12 | 13 | 14 | 15 | 16 | 17
21 | 22 | 23 | 24 | 25 | 26 | 27
11 | 12 | 13 | 14 | 15 | 16 | 17
1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
108
Stage 1
Channel 0
Channel 6
neuron activation

## Slide 69
NA Cache
8 | 2 | 3 | 4 | 5 | 6 | 7
11 | 12 | 13 | 14 | 15 | 16 | 17
21 | 22 | 23 | 24 | 25 | 26 | 27
11 | 12 | 13 | 14 | 15 | 16 | 17
1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
138
Stage 2
8 | 2 | 3 | 4 | 5 | 6 | 7
18 | 12 | 13 | 14 | 15 | 16 | 17
28 | 22 | 23 | 24 | 25 | 26 | 27
18 | 12 | 13 | 14 | 15 | 16 | 17
8 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
117
Stage 4
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 12 | 13 | 14 | 15 | 16 | 17
28 | 22 | 23 | 24 | 25 | 26 | 27
18 | 12 | 13 | 14 | 15 | 16 | 17
8 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
147
Stage 5
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
neuron activation

## Slide 70
NA Cache
8 | 2 | 3 | 4 | 5 | 6 | 7
18 | 12 | 13 | 14 | 15 | 16 | 17
21 | 22 | 23 | 24 | 25 | 26 | 27
11 | 12 | 13 | 14 | 15 | 16 | 17
1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
108
Stage 3
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
neuron activation

## Slide 71
NA Cache
8 | 2 | 3 | 4 | 5 | 6 | 7
18 | 12 | 13 | 14 | 15 | 16 | 17
28 | 22 | 23 | 24 | 25 | 26 | 27
18 | 12 | 13 | 14 | 15 | 16 | 17
8 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
117
Stage 4
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
neuron activation

## Slide 72
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 12 | 13 | 14 | 15 | 16 | 17
28 | 22 | 23 | 24 | 25 | 26 | 27
18 | 12 | 13 | 14 | 15 | 16 | 17
8 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
147
Stage 5
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
neuron activation

## Slide 73
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 22 | 23 | 24 | 25 | 26 | 27
18 | 12 | 13 | 14 | 15 | 16 | 17
8 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
117
Stage 6
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
neuron activation

## Slide 74
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
126
Stage 7
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
neuron activation

## Slide 75
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
156
Stage 8

## Slide 76
NA Cache
……………

## Slide 77
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
156
Stage 15

## Slide 78
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1
1
1
153
Stage 16
1 | 1
1 | 1
1 | 1

## Slide 79
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1
1
1
183
Stage 17
1 | 1
1 | 1
1 | 1

## Slide 80
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1
1
1
153
Stage 18
1 | 1
1 | 1
1 | 1

## Slide 81
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1
1
1
162
Stage 19
1 | 1
1 | 1
1 | 1

## Slide 82
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1
1
1
192
Stage 19
1 | 1
1 | 1
1 | 1

## Slide 83
NA Cache
8 | 9 | 3 | 4 | 5 | 6 | 7
18 | 19 | 13 | 14 | 15 | 16 | 17
28 | 29 | 23 | 24 | 25 | 26 | 27
18 | 19 | 13 | 14 | 15 | 16 | 17
8 | 9 | 3 | 4 | 5 | 6 | 7
1
1
1
162
Last Stage 21
1 | 1
1 | 1
1 | 1

## Slide 84
Filter Cache

## Slide 85
Filter Weight Cache
36 x 16 = 576 Bytes

## Slide 86
Quantization

## Slide 87: Convolutional Neural Networks (CNNs)
  Value Quantization
  -------(1)
  : float/double float value
  : scale
  : quantized value (integer) of
  : quantized value (integer) of

## Slide 88: Convolutional Neural Networks (CNNs)
  Convolution Quantization
  ---(2)
with equation (1)

## Slide 89: Convolutional Neural Networks (CNNs)
  Convolution Quantization
  ---(2)

## Slide 90: Convolutional Neural Networks (CNNs)
  Convolution Quantization

## Slide 91: Convolutional Neural Networks (CNNs)
  Convolution Quantization
is 0 in Computer Version.

## Slide 92: Convolutional Neural Networks (CNNs)
  Convolution Quantization
is 0 in Computer Version.

## Slide 93: Convolutional Neural Networks (CNNs)
  Convolution Quantization
  ---(2)
The result is not int8 but int32 !!!
In TensorFlow, the result needs to be re-quantized.

## Slide 94: Convolutional Neural Networks (CNNs)
  Convolution Quantization
  ---(2)
  With equation (1)
The result is not int8 but int32 !!!
In TensorFlow, the result needs to be re-quantized.

## Slide 95: Convolutional Neural Networks (CNNs)
  Convolution Quantization
  ---(2)
  With equation (1) ->
The result is not int8 but int32 !!!
In TensorFlow, the result needs to be re-quantized.

## Slide 96: Convolutional Neural Networks (CNNs)
  Convolution Quantization
  With equation (2)
We need to know and to get the re-quantized .

## Slide 97: Convolutional Neural Networks (CNNs)
  Convolution Quantization
  As , and the maximum (255) and minimum (0) value of are known, obtaining the maximum and minimum value of , and can be calculated.